## Slide 1: OPERATING SYSTEMS (CS F372) I/O Systems
Barsha Mitra
CSIS Dept., BITS Pilani, Hyderabad Campus

## Slide 2
Overview
Ports, buses, device controllers connect to various devices
Device drivers encapsulate device details, hides differences among I/O controllers from I/O subsystem of kernel
Signals from I/O devices interface with computer
Port – connection point for device
Bus – set of wires and a protocol
    PCI bus, expansion bus
Controller – electronics that operate port, bus, device
    Sometimes integrated on a chip
    Sometimes separate circuit board plugging into the computer, contains processor, microcode, private memory

## Slide 3
I/O Hardware
I/O instructions control devices
Controllers usually have registers where device driver places processor commands, addresses, and data to write, or read data from registers after command execution
Data-in register – read by processor to get i/p
Data-out register – written by processor to send o/p
Status register – contains bits that can be read by processor, bits indicate states like completion of current command, availability of byte to be read from data-in register or occurrence of device error
Control register – written by processor to start a command

## Slide 4
Polling
CPU reads busy bit from status register until 0
CPU sets read or write bit in command register and if write bit is set, writes a data byte into data-out register
CPU sets command-ready bit in command register
Controller sees command-ready bit and sets busy bit
Controller sees write command in command register, reads byte from data-out register and complete I/O
Controller clears busy bit, error bit (status reg.), command-ready bit when transfer done
Step 1 is busy-waiting or polling
  Reasonable if device is fast, but inefficient if device slow
  CPU switches to other tasks?
    How does CPU know controller is idle, controller buffer may overflow

## Slide 5
I/O Interface
Device Types
  Character-stream or block
  Sequential or random-access
  Synchronous or asynchronous
  Sharable or dedicated
  Speed of operation
  read-write, read only, or write only

## Slide 6
I/O Interface
Block & Character Devices
Block devices include disk drives
Character devices include keyboards, mice
Types of I/O
Blocking
Nonblocking – input from keyboard and mouse
Asynchronous – disk and n/w I/O

## Slide 7
Other Aspects
Error Handling
OS can recover from disk read, device unavailable, transient write failures
  Retry a read or write, for example
Most return an error number or code when I/O request fails
System error logs hold problem reports
I/O Protection
User process may accidentally or purposefully attempt to disrupt normal operation via illegal I/O instructions
  All I/O instructions defined to be privileged
  I/O must be performed via system calls

## Slide 8
Thank You